Overflow Room Bridge Setup [2223 (( 2103]

Audio Bridge:

Note: This process will be removed once the TPC Audia Presets are working…

The Audia Program:

- Find and open the Audia Icon on the desktop. Looks like a lower case “a” in a round red dot.

- On the long tool bar with icons, look for the one called “Connect”. It will have a yellow hew to it. Best way to describe it would be a cap “T” with a shaded box on the vertical line.

- Double Click on this icon

- Note: An error/fault message may appear. This is “OK”, go ahead and click “Yes”

- A Dialog box called “System Connect” should appear.

- Look for “Room2103”, click on it to highlight it. Note: This file will not appear if the room is not turned on.

- Click on the “Connect to System” button located on the right hand side of the dialog box.

- Check: If all is working well, you should see the numbers on most of the VU meters fluctuate. Maybe even going up and down due to some audio that is currently being used.

Turning on room 2223 audio/PA so that it comes out the room speakers of room 2103

- Locate a pinkish box called “EXPI, 8 Channel” --- should be the upper left one.

- Double click on it to open a dialog box

- A dialog box should appear on symmetric somewhere called “EXPI 8 Channel”

- It will show inputs 1 through 8 vertically.

- Locate input number 8 and un-mute it by clicking on the number 8 it’s self. You will see the red(light) dot go off or on depending that state it was in.

- When the red(lights) dots are on or lit this means that input is muted. When the red(lights) dots are off or not lit this means that input is “not” muted and that audio signal is free to go beyond that point within the symmetric.

- We need Channel 8 to be un-muted, the red(light) dot must be off.